# StonePly™

# Translucent Stone Panels.

SECTION  07420 - NATURAL STONE REINFORCED PANELS (EXTERIOR)

SECTION 09452 -  NATURAL STONE REINFORCED PANELS (INTERIOR)

This section is based on the products of

StonePly

Suite A, 4400 Oneal

Greenville, TX  75404

Tel: (903) 454-0904

Fax: (903) 454-3642

www.stoneply.com

Verify lead times on custom items.

## PART 1 GENERAL

### 1.1 	SECTION INCLUDES

- StonePly Translucent Panels

1.2	WORK INCLUDED

- Furnish all materials, labor, tools, equipment engineering, and services to install composite stone panels of natural stone bonded to Translucent backing.

### 1.3 	RELATED SECTIONS

- Section 08630 - Metal-Framed Skylights.

- Section 07900 - Joint Sealers.

- Section 08800 - Glazing

### 1.4	REFERENCES

- ASTM Z 97.1 - American National Standard for Glazing Materials Used in Buildings -- Safety Performance Specifications and Methods of Test.

- G. ASTM F 1233 - Standard Test Method for Security Glazing Materials and Systems.

1.5	QUALITY ASSURANCE

- Manufacturer Qualifications: The stone panel manufacturer shall have at minimum a 3 year demonstrated capability to produce panels of the quality and scope required.

- Installer Qualifications:  Regularly engaged and experienced in the installation of composite natural stone veneer panels.

### 1.6 	SUBMITTALS

- Submit under provisions of Section 01300.

- Product Data: Manufacturer's data sheets on each product to be used, including:

  - Physical properties including data on material weight, light transmission and thermal expansion.

  - Preparation instructions and recommendations

  - Storage and handling requirements and recommendations.

  - Installation methods and procedures, including edge engagement guidelines.

- Verification Samples: Submit samples for each finish product specified, two samples, minimum size 2 inches by 3inches, representing actual product.

### 1.7 	DELIVERY, STORAGE, AND HANDLING

- Deliver StonePly Translucent panels on enclosed boxes and pallets.

- Store products in manufacturer's unopened packaging until ready for installation.

- Store in dry, well-ventilated and covered areas at temperatures below 90 degrees F.

- Handle sheets carefully to prevent damage; do not drop, slide, or drag.

### 1.8 	PROJECT CONDITIONS

- Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results. Do not install products under environmental conditions outside manufacturer's absolute limits.

### 1.9	 WARRANTY

- Provide StonePly Translucent Panels manufacturer's written warranty covering breakage.

## PART 2 PRODUCTS

### 2.1 	MANUFACTURERS

- Provide products manufactured by StonePly Inc 4400 Oneal Street, Greenville, TX 75401 Tel (903) 454-0904 Fax (903) 454-3642 info@stoneply.com www.stoneply.com

- Substitutions are not allowed.

### 2.2 	MATERIALS

- The stone shall match the sample:

  - Stone Finish shall be: (select one) [polished] [honed] [to match the approved sample]

- StonePly Panels - General: Comply with properties as follows:

- Panel Thickness: _______.

- Backing Material:  (Select One) [Glass] [Polycarbonate] [As indicated on drawings].

- Stone Selection: _______.

- Dimensional Tolerance:  Plus or minus 1/8” (3.2mm) in all directions.  Plus or minus 1/8” (3.2mm) diagonally.

2.3	ACCESSORIES

- Joint sealants (as specified in section 07920) shall be pre tested for compatibility with the natural stone panel facing selected.

## PART 3 EXECUTION

### 3.1 	EXAMINATION

- Inspect pallets upon delivery for evidence of damage.

- Inspect and verify that openings are correct size and conform to recommendations of the StonePly Translucent Stone Panel manufacturer.

### 3.2 	PREPARATION

- Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

- Immediately prior to installation, expose glazing edges of stone panel by peeling back factory-applied protective masking to a dimension sufficient for edge engagement.

### 3.3 	INSTALLATION

- Install StonePly translucent in accordance with manufacturer's recommendations for edge engagement and expansion allowance.

- Employ only sealants and glazing accessories that have been approved by manufacturer of StonePly translucent panels.

- Remove protective masking immediately after all installation operations are completed.

### 3.4 	PROTECTION

- Protect installed products until completion of project.

- Affix polyethylene film or other approved covering to framing members, as required to protect StonePly translucent stone panels from other construction operations.

- Repair or replace damaged products before Substantial Completion.

- Clean all dirt, marks, & sealant from stone panels using methods appropriate for the type of stone and per manufacturer’s recommendation.

### 3.5 	SCHEDULE

*  This paragraph to be provided by the architect.  *

END OF SECTION